## Slide 1
Feature: Individual measurable property or characteristic of a phenomenon being observed

## Slide 2: Feature Example
x | -1.4
y | 0.4
z | 9.6
Acceleration (m/s2)
Model
Left-right
Up-down
Circle
Idle

## Slide 3
1 (x, y, z) accelerometer point from “left-right” sample
Many (x, y, z) accelerometer points from all classes

## Slide 4: Feature Example
x | -1.4 | -1.4 | -2.8 | -3.4 | -4.0
y | 0.4 | 0.4 | 0.1 | 0.2 | 0.3
z | 9.6 | 9.6 | 9.9 | 9.7 | 9.8
Acceleration (m/s2)
Model
Left-right
Up-down
Circle
Idle
...
...
...
125 samples for each axis
...
...
375 total inputs to the model!
2 second window

## Slide 5: Problems with deep learning
Computational complexity
Requires lots of training data
High-dimensional inputs
Neural network for extracting features
Neural network for classifying
Class 1
Class 2
Class 3
Class 4

## Slide 6: Feature Example
x | -1.4 | -1.4 | -2.8 | -3.4 | -4.0
y | 0.4 | 0.4 | 0.1 | 0.2 | 0.3
z | 9.6 | 9.6 | 9.9 | 9.7 | 9.8
Acceleration (m/s2)
Model
Left-right
Up-down
Circle
Idle
...
Feature extraction:
Calculate RMS for each axis
...
...
...
...
375 raw values
3 model input values
xRMS = 5.7 m/s2 (RMS)
yRMS = 1.2 m/s2 (RMS)
zRMS = 9.9 m/s2 (RMS)
2 second window

## Slide 8
Feature extraction:
FFT
m/s2
m/s2
ms
Hz
Time domain
Frequency domain

## Slide 9
Feature extraction:
FFT
m/s2
ms
Hz
m/s2
Feature extraction:
PSD
[m/s2]2/Hz
Hz
Power Spectral Density (PSD)

## Slide 10: Feature Example
x | -1.4 | -1.4 | -2.8 | -3.4 | -4.0
y | 0.4 | 0.4 | 0.1 | 0.2 | 0.3
z | 9.6 | 9.6 | 9.9 | 9.7 | 9.8
Acceleration (m/s2)
Model
Left-right
Up-down
Circle
Idle
...
Feature extraction:
RMS and Power Spectral Density (PSD)
...
...
...
...
375 raw values
2 second window
33x features
11 features per axis: RMS, 3x peak amplitudes from PSD, 3x peak frequencies from PSD, 4x spectral bins

## Slide 11: Feature Example
x | -6.8 | -5.6 | -4.6 | -4.1 | -3.8
y | -0.1 | 0.2 | 0.7 | 0.9 | 0.7
z | 10.4 | 10.3 | 10.2 | 10.1 | 9.6
Acceleration (m/s2)
Model
Left-right
Up-down
Circle
Idle
...
Feature extraction:
RMS and Power Spectral Density (PSD)
...
...
...
...
375 raw values
2 second window
33x features
11 features per axis: RMS, 3x peak amplitudes from PSD, 3x peak frequencies from PSD, 4x spectral bins